## Slide 1: Development of a Spectral Element Method-based Incompressible Flow Solver MTP Phase 2 Presentation By Nishant Jagtap (234103329) Under the guidance of Dr. Atul Kumar Soti
Department of Mechanical Engineering
Indian Institute of Technology Guwahati, Assam
June 2024

## Slide 2: Outline
Introduction
Objective
Literature Review
Spectral Element Method (SEM)
Navier-Stokes equation
Element-by-element Conjugate Gradient
PETSC and CG Solver
Results
Summary and Future work

## Slide 3: Introduction
Spectral Element Method (SEM) combines the Geometric flexibility of the Finite Element method with the accuracy of the Spectral Method.
  High-order convergence for smooth solutions with fewer degrees of freedom
  High accuracy per degree of freedom ( higher-order polynomials )
  Compatible with coarse mesh and parallel computing architecture
  Better resolution of boundary layers and vortices
Weak formulation of the governing equation
Transformation to the elemental level
Transforming Physical domain to Computational domain
Approximation of the unknown variable in terms of Lagrange polynomials
Numerical Integration based on Gauss Legendre Lobatto Quadrature
Formulation of Mass, Differential and Laplacian Matrix for single element
Global Assembly of matrices using Connectivity matrix
Solving Linear System of Equations to obtain required solutions
Form Linear System of Equations from Global Matrices
Boundary Conditions on Linear system of equation
Notes: SEM = SM + FEM
Compare with FDM and FVM
Give background of senior’s work
Ladyzenskaya Babuska Brezzi (LBB) or inf-sup conditions

## Slide 4: Objective
Develop a solver to accommodate unequal order interpolation for velocity and pressure using the Taylor-Hood Element.
Implementing the Element-by-Element level approach to avoid global assembly for efficient computation and reduce memory requirements.
Extend the FEM approach to SEM approach
Correct Lift-Drag Calculation for Flow over Bluff Bodies
Generate CSR matrices and develop an in-house CG Solver
Test the solver and validate the results against major fluid flow test problems

## Slide 5: Literature Review
Author | Work
Patera, 1984 [1] | Introduced the spectral element for the first time using Chebyshev collocation points using Chebyshev interpolation for solving laminar flow in channel.
C. Taylor and P. Hook, 1973 [28] | Implemented 2nd order interpolation for velocity and 1st order interpolation for pressure to solve constrained flow problems to avoid checkerboarding condition.
Fischer and Rønquist, 1994 [10] | Used Preconditioned Conjugate Gradient Method to optimize computational time and memory with domain decomposition.
J. Kim and P. Moin, 1985 [16] | Applied fractional-step method to solve incompressible Navier-Stokes equations.
Jiang and Cheng (2021) [12] | Nektar++ achieved mesh convergence at 3% computational cost compared to OpenFOAM's estimated one million core hours.

## Slide 6: Galerkin FEM
Model Problem: 1D Poisson’s equation
Weak formulation: Approximate the variables q and f using nodal expansion:
Differential equation reduces to
Figure 1: 1D Domain
Imposing orthogonality between test function and residual , | Applying Homogeneous Neumann Boundary condition and using Integration by parts
= 0 | 
 | Applying Homogeneous Neumann Boundary condition and using Integration by parts
=0

## Slide 7
and are test function and basis functions respectively
For 1st order interpolating function for 1D system, the above equation at elemental level can be represented as:
Representation in Matrix form:
=

## Slide 8: Interpolating Polynomials and Roots
Nth order Lagrange polynomials are used as basis functions with nodes as roots of (N+1)th order Lobatto polynomial
Lagrange Polynomials 
The Legendre polynomial [ & are used to find out Lobatto polynomials
,
where, &
Lobatto Polynomial
Figure 2: Roots of Lobatto polynomial in 1D [6]
Notes: Equidistant points
Can be extended to SEM

## Slide 9: Global Assembly
Figure 3(b): Global Assembly in 1D domain
I = J = | 
Connectivity Matrix
Figure 3(a): Global Assembly

## Slide 10: Boundary Conditions
Here, the left and right nodes are Dirichlet boundary conditions
They are eliminated from the matrices to form modified system of equations

## Slide 11: 2D Domain
:
:
:
:
Figure 4(b): Global Assembly in 2D domain
Figure 4: 2D domain and Connectivity matrix

## Slide 12: Navier-stokes Equation & Fractional Step Method
Governing Equations (Non-dimensional form)
Step 1
Step 2
Step 3
Temporal term : 1st order Forward Difference
Convective term : Adams-Bashforth Method
Diffusion term : Crank-Nicolson Scheme
Fractional Step Method
Continuity Equation
Momentum Equation

## Slide 13: Global System of Equations
Mass Matrix | =
Laplacian Matrix | 
Differential Matrix | 
Mass Matrix | 
Laplacian Matrix | 
Differential Matrix | 
System of Equations

## Slide 14: Taylor-Hood Element
Ensure numerical stability and avoid spurious pressure modes
Uses piecewise continuous quadratic velocities and piecewise continuous linear pressures
1st order interpolation for pressure within an element
2nd order interpolation for velocity within an element
Figure 5(a): Pressure Expansion function
Figure 5(b): Velocity Expansion function

## Slide 15: Element-by-Element Conjugate Gradient Method
=

## Slide 16: Results – Lid driven Cavity
Elements |  |  | 
Order (N1,N2) | V=2, P=1 | V=3, P=2 | V=6, P=4
Total Nodes | (1681,441) | (3721,1681) | (14641,6561)
Re | 100 | 100 | 100
Elements |  |  | 
Order (N1,N2) | V=2, P=1 | V=3, P=2 | V=6, P=4
Total Nodes | (1681,441) | (3721,1681) | (14641,6561)
Re | 100 | 100 | 100
At Re=100, the solution was computed at different interpolating orders of velocity and pressure.
As order of interpolating polynomial increases, the solution becomes more accurate
(4,3) interpolating order is chosen for further analysis
Red & Black : Velocity ( order)
Black : Pressure ( order)
Figure 6(a): Geometry and BCs
Figure 6(b): Meshing
Numerical Simulation Parameters

## Slide 17
Figure 7(a): u velocity variation with y at mid-vertical line (x=0.5) at Re=100
Figure 7(b): v velocity variation with x at mid-horizontal line (y=0.5) at Re=100

## Slide 18
Elements |  |  | 
Order | V=4, P=3 | V=4, P=3 | V=4, P=3
Total Nodes | (6561,3721) | (6561,3721) | (6561,3721)
Re | 100 | 400 | 1000
Elements |  |  | 
Order | V=4, P=3 | V=4, P=3 | V=4, P=3
Total Nodes | (6561,3721) | (6561,3721) | (6561,3721)
Re | 100 | 400 | 1000
Figure 8(a): Variation of u velocity with y at mid-vertical line (x=0.5)
Figure 8(b): Variation of v velocity with x at mid-horizontal line (y=0.5)
Numerical Simulation Parameters

## Slide 19: Code Restructuring & Solver Update
Element-by-element Assembly Approach
Global A Matrix not stored
In , only the matrix-vector product is assembled from element-level matrices to form the global vector = Ax
Global A Matrix not stored
In 𝐴𝑥=𝑏, only the matrix-vector product is assembled from element-level matrices to form the global vector = Ax
All operations can be parallelized at the element level
Global Assembly Approach
Global Matrix is formed in CSR format
Can use multiple preconditioners and solvers; many numerical libraries are available
Only Jacobi preconditioner can be easily applied
Repetitive Assembly operations for the matrix-vector product for each iteration of each timestep
Many commercial library Solvers
Single-assembly operation
Absence of element-level parallelization
Element-by-element Assembly Approach
All operations can be parallelized at the element level
Global Assembly Approach
Global Matrix is formed in CSR format
Can use multiple preconditioners and solvers; many numerical libraries are available
Only Jacobi preconditioner can be easily applied
Repetitive Assembly operations for the matrix-vector product for each iteration of each timestep
Many commercial library Solvers
Single-assembly operation
Absence of element-level parallelization




X
X
X

## Slide 20: PETSC Solver
“Portable, Extensible Toolkit for Scientific Computation”
  (open-source computing library)
Iterative linear solver  KSP CG
Preconditioners: Jacobi, ILU, GAMG
Matrix stored in CSR format
Limitations:
  Requires all vectors and matrices in PETSC format
  Limits parallelization control as per the user's discretion
  Enforces PETSC installation for code execution
Figure 9: PETSC Solver Structure

## Slide 21: CG Solver
Global Matrix stored in CSR format
  (Assembled using Compressed Matrix format)
Uses BLAS library for matrix-vector multiplication
Without preconditioner and with Jacobi preconditioner in the current implementation.
Other preconditioners can be implemented
Method | Average Iterations |  |  | Computational Time
 |  |  | Pressure | 
PETSC CG (Jac) | 4 | 5 | 288 | 3678.5464
Solver CG (Jac) | 2 | 3 | 289 | 2185.8981
Method | Average Iterations |  |  | Computational Time
 |  |  | Pressure | 
PETSC CG (Jac) | 4 | 5 | 288 | 3678.5464
Solver CG (Jac) | 2 | 3 | 289 | 2185.8981
Method | Average Iterations |  |  | Computational Time
 |  |  | Pressure | 
PETSC CG (None) | 181 | 344 | 312 | 19327.276
Solver CG (None) | 193 | 358 | 319 | 10930.507
Method | Average Iterations |  |  | Computational Time
 |  |  | Pressure | 
PETSC CG (None) | 181 | 344 | 312 | 19327.276
Solver CG (None) | 193 | 358 | 319 | 10930.507
Table 2: Results for CG with Jacobi Preconditioner
No. of timesteps | 50000
Tolerance | 1.00E-09
Order (Vel, Pres) | 2,1
Nodes (Vel, Pres) | 21826, 5513
Quad Elements | 5400
Table 1: Results for CG with No Preconditioner
Numerical Simulation Parameters
Figure 10: Comparison of the lift-drag coefficient of the in-house CG Solver with the PETSC solver
Global Assembly in Compressed Matrix Format
CSR matrix
CG Solver

## Slide 22: Creation of CSR Matrix
Direct Solvers and other preconditioners can be directly applied
 | 1 | 2 | 3 | 4 | 5 | 6
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6
1 | -1 | -1 | -1 | -1 | -1 | -1
2 | -1 | -1 | -1 | -1 | -1 | -1
3 | -1 | -1 | -1 | -1 | -1 | -1
4 | -1 | -1 | -1 | -1 | -1 | -1
5 | -1 | -1 | -1 | -1 | -1 | -1
6 | -1 | -1 | -1 | -1 | -1 | -1
Compressed Matrix Storage
Compressed Sparse Row (CSR) Storage
Values matrix
Column indices matrix
Initialization
Figure 11: Storage of Sparse Matrices

## Slide 23: Global Assembly in Compressed Matrix
1 | 2 | 4 | 5
2 | 3 | 5 | 6
Element 1
Element 2
2
1
 | 1 | 2 | 3 | 4 | 5 | 6
1 | 1 | 2 | 4 | 5 |  | 
2 | 1 | 2 | 4 | 5 | 3 | 6
3 | 2 | 3 | 5 | 6 |  | 
4 | 1 | 2 | 4 | 5 |  | 
5 | 1 | 2 | 4 | 5 | 3 | 6
6 | 2 | 3 | 5 | 6 |  | 
3
4
 | 1 | 2 | 3 | 4 | 5 | 6
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6
1 |  |  |  |  |  | 
2 |  | + |  | + |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  | + |  | + |  | 
6 |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6
1 | 1 | 2 | 4 | 5 |  | 
2 | 1 | 2 | 4 | 5 |  | 
3 |  |  |  |  |  | 
4 | 1 | 2 | 4 | 5 |  | 
5 | 1 | 2 | 4 | 5 |  | 
6 |  |  |  |  |  | 
Values matrix
Column indices matrix
Assembling Element 1
Assembling Element 2
Figure 12(a): Element-level Mass matrix
Figure 12(c): Connectivity matrix
Figure 12(b): Domain

## Slide 24: Converting Compressed Matrix to CSR Matrix
 | 1 | 2 | 3 | 4 | 5 | 6
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6
1 | 1 | 2 | 4 | 5 |  | 
2 | 1 | 2 | 3 | 4 | 5 | 6
3 | 2 | 3 | 5 | 6 |  | 
4 | 1 | 2 | 4 | 5 |  | 
5 | 1 | 2 | 3 | 4 | 5 | 6
6 | 2 | 3 | 5 | 6 |  | 
1 | 5 | 11 | 15 | 19 | 25 | 29
1 | 2 | 4 | 5 | 1 | 2 | 3 | 4 | 5 | 6
2 | 3 | 5 | 6 | 1 | 2 | 4 | 5
1 | 2 | 3 | 4 | 5 | 6 | 2 | 3 | 5 | 6
Row Pointer Array
Values Array
Column Indices Array
Values matrix
Column indices matrix
Compressed Matrix sorted in ascending order of column indices for each row
CSR Matrix

## Slide 25: SEM Mesh Generation
Fortran-based
Reads data from GMSH file
Generates SEM mesh using Lobatto points inside each element
Global node numbering in order of boundary nodes , interface nodes, and internal nodes (very useful to eliminate boundary nodes from the global matrix and performing parallel programming)
Stores neighbouring element data useful for moving mesh
Figure 13: SEM Mesh Generation

## Slide 26: Curved Mesh
Second-order shape functions are used in each directions
8-noded Shape quadrilateral
Figure 12(b): First-order Mesh unable to capture curvature
Figure 12(a): Curved Mesh

## Slide 27: Lift-Drag Calculation
 | INTEGRATION | NUMERICAL INTEGRATION
Lift Force |  | 
Drag Force |  | 
 | INTEGRATION | NUMERICAL INTEGRATION
Lift Force |  | 
Drag Force |  | 
Form Lift/Drag
Skin Friction Lift/Drag
Viscous Drag and Lift
Figure 13(a): Lift-Drag forces
Figure 13(b): Lift and Drag forces components

## Slide 28
No. of timesteps | 50000
Tolerance | 1.00E-06
Order (Vel, Pres) | 4,4
Nodes (Vel, Pres) | 6204, 6204
Quad Elements | 378
Reynolds No. | 100
Flow over Circular Cylinder
Figure 14(a): CC - Gmsh Coarse Mesh
Figure 14(b): CC - 4th order SEM Mesh
Figure 14(c): CC - Geometry and Boundary Conditions
Numerical Simulation Parameters

## Slide 29: FEM vs SEM Results
Preconditioner | Quad elements | Velocity & Pressure Nodes | Average Iterations/timestep |  |  | Computational Time (s)
 |  |  |  |  | Pressure | 
Jacobi Preconditioner | 5400 | 21826, 5513 (Order = 2,1) | 4 | 5 | 288 | 3674
ILU Preconditioner |  |  | 2 | 2 | 68 | 2820
Preconditioner | Quad elements | Velocity & Pressure Nodes | Average Iterations/timestep |  |  | Computational Time (s)
 |  |  |  |  | Pressure | 
Jacobi Preconditioner | 5400 | 21826, 5513 (Order = 2,1) | 4 | 5 | 288 | 3674
ILU Preconditioner |  |  | 2 | 2 | 68 | 2820
Order of Interpolation | Quad elements | Velocity & Pressure Nodes | Average Iterations/timestep |  |  | Computational Time (s) | Absolute Error (%) | 
 |  |  |  |  |  |  | Lift () | Drag ()
 |  |  |  |  | Pressure |  |  | 
2nd order | 378 | 1590, 1590 | 1 | 1 | 20 | 617 | 24.567 | 0.7380
3rd order |  | 3519, 3519 | 1 | 1 | 34 | 2648 | 4.10753 | 1.1070
4th order |  | 6204, 6204 | 1 | 1 | 46 | 4576 | 0.20147 | 0.1476
5th order |  | 9645, 9645 | 1 | 1 | 53 | 8382 | 0.1173 | 0.0780
6th order |  | 13842, 13842 | 1 | 1 | 60 | 10254 | 0 | 0
Order of Interpolation | Quad elements | Velocity & Pressure Nodes | Average Iterations/timestep |  |  | Computational Time (s) | Absolute Error (%) | 
 |  |  |  |  | Pressure |  |  | 
2nd order | 378 | 1590, 1590 | 1 | 1 | 20 | 617 | 24.567 | 0.7380
3rd order |  | 3519, 3519 | 1 | 1 | 34 | 2648 | 4.10753 | 1.1070
4th order |  | 6204, 6204 | 1 | 1 | 46 | 4576 | 0.20147 | 0.1476
5th order |  | 9645, 9645 | 1 | 1 | 53 | 8382 | 0.1173 | 0.0780
6th order |  | 13842, 13842 | 1 | 1 | 60 | 10254 | 0 | 0
Lower number of elements
Lower number of nodes
Less computational time
Higher accuracy
FEM
SEM
Table 3: CC - FEM Results
Table 4: CC - SEM Results

## Slide 30
 | Numerical Results |  | 
 | Mean Value | Peak Value | RMS value
Form Lift Coefficient ( | 0 | 0.2918 | 0.206122
Form Drag Coefficient ( | 1.02 | - | -
Skin friction Lift Coefficient | 0 | 0.04535 | 0.0320673
Skin friction Drag Coefficient () | 0.3475 | - | -
Total Lift Coefficient ( | 0 | 0.332 | 0.23476
Total Drag Coefficient () | 1.35 | - | -
 | Numerical Results |  | 
 | Mean Value | Peak Value | RMS value
 | 0 | 0.2918 | 0.206122
 | 1.02 | - | -
 | 0 | 0.04535 | 0.0320673
 | 0.3475 | - | -
 | 0 | 0.332 | 0.23476
 | 1.35 | - | -
 | SEM (4,4) (Present) | Park et al[37]. | Absolute Error (%)
(mean) | 1.01 | 0.99 | 2.020
(mean) | 1.35 | 1.33 | 1.504
(rms) | 0.2347 | 0.235 | 2.043
Strouhal Number () | 0.164 | 0.165 | 0.165
 | SEM (4,4) (Present) | Park et al[37]. | Absolute Error (%)
 | 1.01 | 0.99 | 2.020
 | 1.35 | 1.33 | 1.504
 | 0.2347 | 0.235 | 2.043
 | 0.164 | 0.165 | 0.165
Flow over Circular Cylinder
Figure 15(a):
Vortex Shedding
Figure 15(b):
Lift Coefficient
Table 5: CC- Lift-Drag Coefficients
Table 6: CC-Validation

## Slide 31: Flow over Square Cylinder
No. of timesteps | 50000
Tolerance | 1.00E-06
Order (Vel, Pres) | 4,4
Nodes (Vel, Pres) | 4848, 4848
Quad Elements | 294
Reynolds No. | 100
Figure 16(b): SC - 4th order SEM Mesh
Figure 16(a): SC - Gmsh coarse Mesh
Figure 16(c): SC - Geometry and Boundary Conditions
Numerical Simulation Parameters

## Slide 32: Flow over Square Cylinder
Order of Interpolation | Quadrilateral elements | Velocity and Pressure Nodes | Average Iterations/timestep |  |  | Computational Time (s) | Absolute Error (%) (Total Mean Drag)
 |  |  |  |  | Pressure |  | 
2nd order | 294 | 1248, 1248 | 1 | 1 | 21 | 914 | 4.006
3rd order |  | 2754, 2754 | 1 | 1 | 32 | 1645 | 4.006
4th order |  | 4848, 4848 | 1 | 1 | 41 | 2222 | 1.054
5th order |  | 7530, 7530 | 1 | 1 | 49 | 5192 | 0.3514
6th order |  | 10800 ,10800 | 1 | 1 | 56 | 8949 | 0
Order of Interpolation | Quadrilateral elements | Velocity and Pressure Nodes | Average Iterations/timestep |  |  | Computational Time (s) | Absolute Error (%) (Total Mean Drag)
 |  |  |  |  | Pressure |  | 
2nd order | 294 | 1248, 1248 | 1 | 1 | 21 | 914 | 4.006
3rd order |  | 2754, 2754 | 1 | 1 | 32 | 1645 | 4.006
4th order |  | 4848, 4848 | 1 | 1 | 41 | 2222 | 1.054
5th order |  | 7530, 7530 | 1 | 1 | 49 | 5192 | 0.3514
6th order |  | 10800 ,10800 | 1 | 1 | 56 | 8949 | 0
4th order SEM Mesh | SEM (4,4) (Present) | Zhao[40] | Absolute Error (%)
(mean) | 1.438 | 1.45 | 3.263
(rms) | 0.189 | 0.188 | 0.32
Strouhal Number () | 0.144 | 0.145 | 1.53
4th order SEM Mesh | SEM (4,4) (Present) | Zhao[40] | Absolute Error (%)
 | 1.438 | 1.45 | 3.263
 | 0.189 | 0.188 | 0.32
 | 0.144 | 0.145 | 1.53
Figure 17(a): SC – u velocity (t = 50 s)
Figure 17(b): SC – u velocity (t = 200 s)
Figure 17(c): SC – Lift Coefficient
Table 7: SC - Results for various SEM orders for the square cylinder at Re = 100
Table 8: SC-Lift-Drag Validation

## Slide 33: Flow over Elliptical Cylinder
No. of timesteps | 50000
Tolerance | 1.00E-06
Order (Vel, Pres) | 4,4
Nodes (Vel, Pres) | 11588, 11588
Quad Elements | 714
Reynolds number | 150
Numerical Simulation Parameters
Figure 18(a): EC –Gmsh Mesh
Figure 18(b): EC - 4th order SEM Mesh
Figure 18(c): EC – Geometry and Boundary Conditions)

## Slide 34: Flow over Elliptical Cylinder
 | Order of Interpolation | Quadrilateral elements | Velocity and Pressure Nodes | Average Iterations/timestep |  |  | Computational Time (s) | Absolute Error (%) (Total Mean Drag)
 |  |  |  |  |  | Pressure |  | 
Vertical Ellipse | 3rd order | 714 | 6549, 6549 | 1 | 1 | 59 | 3073 | 1.06383
 | 4th order |  | 11588, 11588 | 1 | 1 | 76 | 7704 | 0.53192
 | 5th order |  | 18055, 18055 | 1 | 1 | 87 | 16188 | 0
Horizontal Ellipse | 3rd order | 714 | 6549, 6549 | 1 | 1 | 52 | 5133 | 0.9596
 | 4th order |  | 11588, 11588 | 1 | 1 | 69 | 11545 | 2.0202
 | 5th order |  | 18055, 18055 | 1 | 1 | 82 | 23057 | 0
 | Order of Interpolation | Quadrilateral elements | Velocity and Pressure Nodes | Average Iterations/timestep |  |  | Computational Time (s) | Absolute Error (%) (Total Mean Drag)
 |  |  |  |  |  | Pressure |  | 
Vertical Ellipse | 3rd order | 714 | 6549, 6549 | 1 | 1 | 59 | 3073 | 1.06383
 | 4th order |  | 11588, 11588 | 1 | 1 | 76 | 7704 | 0.53192
 | 5th order |  | 18055, 18055 | 1 | 1 | 87 | 16188 | 0
Horizontal Ellipse | 3rd order | 714 | 6549, 6549 | 1 | 1 | 52 | 5133 | 0.9596
 | 4th order |  | 11588, 11588 | 1 | 1 | 69 | 11545 | 2.0202
 | 5th order |  | 18055, 18055 | 1 | 1 | 82 | 23057 | 0
 |  | Vertical Ellipse |  | Horizontal Ellipse |  | 
4th order SEM Mesh | SEM (4,4) (Present) | Xiaoyu Shi et al[43] | Absolute Error (%) | SEM (4,4) (Present) | Xiaoyu Shi et al[43] | Absolute Error (%)
(mean) | 1.89 | 1.824 | 4.8 | 0.985 | 0.95 | 3.68
(rms) | 0.55861 | 0.53 | 5.4 | 0.10116 | 0.103 | 1.78
Strouhal Number () | 0.2 | 0.191 | 5 | 0.172 | 0.169 | 1.77
 |  | Vertical Ellipse |  | Horizontal Ellipse |  | 
4th order SEM Mesh | SEM (4,4) (Present) | Xiaoyu Shi et al[43] | Absolute Error (%) | SEM (4,4) (Present) | Xiaoyu Shi et al[43] | Absolute Error (%)
 | 1.89 | 1.824 | 4.8 | 0.985 | 0.95 | 3.68
 | 0.55861 | 0.53 | 5.4 | 0.10116 | 0.103 | 1.78
 | 0.2 | 0.191 | 5 | 0.172 | 0.169 | 1.77
Table 10: Results for various SEM orders for the elliptical cylinder at Re = 150
Table 9: Lift-Drag values for the elliptical cylinder at Re = 150
Figure 19(a): EC – Streamlines
Figure 19(b): EC – Vortex Shedding

## Slide 35: Flow over Elliptical Cylinder inclined at
4th Order SEM Mesh | Numerical Simulation |  | Validation Subhankar Sen et al.[45] | 
 | Mean Value | RMS value | Mean value | RMS value
Total Lift Coefficient ( | 0.5012 | 0.15298 | 0.4987 | 0.1531
Total Drag Coefficient () | 1.145 | - | 1.1515 | -
4th Order SEM Mesh | Numerical Simulation |  | Validation Subhankar Sen et al.[45] | 
 | Mean Value | RMS value | Mean value | RMS value
 | 0.5012 | 0.15298 | 0.4987 | 0.1531
 | 1.145 | - | 1.1515 | -
No. of timesteps | 50000
Tolerance | 1.00E-06
Order (Vel, Pres) | 4,4
Nodes (Vel, Pres) | 7796, 7796
Quad Elements | 478
Reynolds number | 100
Numerical Simulation Parameters
Table 11: Lift-Drag calculation for inclined Ellipse
Figure 20: 4th order SEM plots for backward inclined elliptical cylinder at Re = 100
(a) Lift Coefficient
(b) Drag Coefficient
Figure 20(c): backward inclined elliptical cylinder

## Slide 36: Summary & Future Work
SUMMARY
Contributed to the development of a solver for the unsteady, incompressible 2D Navier-Stokes equations
Developed FEM solution for Taylor-Hood element using unequal order interpolating polynomials for pressure and velocity.
Employed the Element-by-Element Conjugate Gradient approach as an alternative to avoid the global assembly approach
Implemented PETSC Solver and in-house CG Solver
Corrected the Lift-Drag calculation
Used curved mesh for capturing curvature using a minimal coarse mesh.
Developed SEM Mesh generation using Fortran code
Simulated and validated the Lid-driven cavity flow problem, flow over circular, square, and elliptical cylinder problems
FUTURE WORK
Completing and enhancing the in-house CG solver and developing direct solvers
Expanding this code to solve Vortex Induced Vibration (VIV) problems and deal with 3D problems
Adapting parallel programming to reduce computational cost
Enable the solver to simulate high Reynolds number flow
Analysis of Fluid Structure Interaction (FSI) problems

## Slide 37: References
[1] A. T. Patera, “A spectral element method for fluid dynamics: Laminar flow in a channel expansion,” J Comput Phys, vol. 54, no. 3, 1984, doi: 10.1016/0021-9991(84)90128-1.
[6] F. X. Giraldo et al., “An Introduction to Element-Based Galerkin Methods on Tensor-Product Bases Analysis, Algorithms, and Applications.”
[10] P. F. Fischer and E. M. Rønquist. “Spectral element methods for large-scale parallel Navier-Stokes calculations”. Computer methods in applied mechanics and engineering 116.1-4 (1994), 69–76.
[12] H. Jiang and L. Cheng, “Large-eddy simulation of flow past a circular cylinder for Reynolds numbers 400 to 3900,” Physics of Fluids, vol. 33, no. 3, Mar. 2021, doi: 10.1063/5.0041168.
[16] J. Kim and P. Moin, “Application of a fractional-step method to incompressible Navier-Stokes equations,” J Comput Phys, vol. 59, no. 2, 1985, doi: 10.1016/0021-9991(85)90148-2.
[28] C. Taylor and P. Hook, “A numerical solution of the navier-stokes equations using the finite element technique,” Pergamoo Press, 1973.
[37] J. Park and H. Choi, “Numerical solutions of flow past a circular cylinder at Reynolds numbers up to 160,” KSME International Journal, vol. 12, no. 6, 1998, doi: 10.1007/BF02942594.
[40] M. Zhao, “Flow-induced vibrations of square and rectangular cylinders at low Reynolds number,” Fluid Dyn Res, vol. 47, no. 2, 2015, doi: 10.1088/0169 5983/47/2/025502.
[43] X. Shi, M. Alam, and H. Bai, “Wakes of elliptical cylinders at low Reynolds number,” Int J Heat Fluid Flow, vol. 82, 2020, doi: 10.1016/j.ijheatfluidflow.2020.108553.
[45] H. Sarkar and S. Sen, “VORTEX-INDUCED VIBRATIONS OF AN ELLIPTIC CYLINDER AT DIFFERENT ANGLES OF INCIDENCE,” in Proceedings of the Thermal and Fluids Engineering Summer Conference, 2023. doi: 10.1615/tfec2023.fna.046072.

## Slide 38
Thank You

## Slide 39: Finite/Spectral Element Method
Weak formulation of the governing equation
Transformation to the elemental level
Transforming Physical domain to Computational domain
Approximation of the unknown variable in terms of Lagrange polynomials
Numerical Integration based on Gauss Legendre Lobatto Quadrature
Formulation of Mass, Differential and Laplacian Matrix for single element
Global Assembly of matrices using Connectivity matrix
Solving Linear System of Equations to obtain required solutions
Form Linear System of Equations from Global Matrices
Boundary Conditions on Linear system of equation

## Slide 40: Numerical Integration
Integrating over domain using Gauss Quadrature Integration 
Lobatto polynomials roots are used as integration points
Corresponding Weights of integration:
(where are degree Legendre Polynomials and are roots of Lobatto polynomials)
degree Lobatto integration points can give an accurate result for integration up to polynomials.

## Slide 41: Element Level Transformation
Figure 3: Domain transformation in 1D
Figure 4: Domain transformation in 2D
1D | 2D
 |  X
1D | 2D
The domain is transformed before integration to have common integration procedure

## Slide 42: Connectivity Matrix
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
j = local node no.
Global Node numbers
1008 | 41 | 5 | 63 | 187 | 78 | 3 | 20 | 56
i = Element no.
Figure 3: Connectivity matrix and SEM Mesh Generation

## Slide 43: Unstructured Grid
Transformation/Shape Functions
Figure 5: Unstructured Grid Element transformation
Notes: Physical to Computational domain
We only read pressure mesh from gmsh file
Reordering the nodes in order >> creating SEM mesh >> Transforming back to physical domain
Jacobian used for transformation and also used in integrals

## Slide 44: Formation of Elemental Level Matrices
Transformation from physical to computational domain and applying numerical integration:
where,
= = =

## Slide 45: Discretising the Governing Equation
Velocity Approximation :
Pressure approximation :
Step 1: Multiplying and integrating equation 1 with test function () corresponding to velocity
Intermediate velocities

## Slide 46
Step 2: Multiplying and integrating equation 2 with test function () corresponding to pressure
Step 3: Multiplying and integrating equation 3 with test function () corresponding to velocity
Pressure Poisson’s equation
Corrected velocities
Notes: Tell the size of all matrices

## Slide 47: Elementary Matrices
(All matrices are defined at element level with a basis and test function of order N)
Mass Matrix | =
Laplacian Matrix | 
Differential Matrix | 
Mass Matrix | 
Laplacian Matrix | 
Differential Matrix | 

## Slide 48: Skin Friction Lift/Drag
Viscous Drag and Lift
Element level Derivative Matrix Calculation
Normal Calculation
2nd order shape functions 

## Slide 49
Lobatto Polynomials
Lobatto polynomial can be obtain from Legendre polynomial from relation
Figure 4: Interpolation of Runge’s function using Equispaced Points(left) and Lobatto Points(right).
Figure 5: Node location from different order of polynomial
Notes: because we are using a finite dimensional polynomial representation, that we cannot exactly satisfy the original homogeneous PDE.